## Slide 1: TEST BENCH
BUG-z, Inc.
A new way to test and validate your applications.

## Slide 2: The Problem
Complex System
Systems are becoming more complex and require interactions of many components.
Human Error
Delayed Testing
Tests are delayed until final assembly which results in significant risks. Changes can be catastrophic and result in delivery delays and financial losses
Timing Constrains
Manual debugging is more prone to error
Scalability
Bigger and more complex scenarios are required to be tested.
Classic debugging approach doesn’t provide real-time simulation

## Slide 3: Solution
Previously mentioned problems can ideally be solved by the following three concepts:
Emulate
Emulate sensors, actuators and any signals necessary before full system completion to prevent delays.
Automate
Writing automated test cases to overcome human error, complexity and timing.
Fix
Early testing will ideally lead to uncovering of defects earlier so they can be fixed.

## Slide 4: Block Diagram
Communication
UDP in direct mode to obtain higher speed. Whilst gRPC uses TCP.
PC
PC is used to input direct values (Direct Mode) or write scripts to be executed on remote target (HIL Mode).
Raspberry Pi
Used as a golden controller with reliable drivers, it applies given values or script to the UUT.
Unit under test
The microcontroller that contains the peripherals that needs to be tested.

## Slide 5
Server/Client | PI Drivers | GUI | RPC
 |  | Python: PyQt | Lorem ipsum dolor sit amet
Implementation Overview
Python -> PyQt
C -> Web sockets (Direct Mode)
Google Remote procedure Call (HIL Mode)
PiGPIO library in Python (HIL Mode) & C (Direct Mode)

## Slide 6: DIRECT MODE
Desired value are directly chosen by the user through the GUI and are cyclically sent to the Pi.

## Slide 7: Frame Format
An agreed upon frame between the PC client and the golden MCU in direct mode.
Chart: 
| Category 1
Signature | 4
Num of CMD | 3
Total Size | 3
PeripheralID | 4
DataSize | 4
Data | 5
... | 6
SIGNATURE
Total Size
Peripheral ID
Data Size
Peripheral Data
Frame Header
Peripheral #1 Data Frame
Peripheral #n Data Frame
CMD #
............

## Slide 8: Flow Control Diagram
Total Cycle
Main Frame

## Slide 9: HIL MODE
A test case script skeleton is generated for the user where they can call the desired APIs on the Pi remotely from their own PC via GRPC.

## Slide 10: Initialization
Server Side
Create Services
Provides services, their parameters and return values.
Server Side
Implement Methods
Provides implementation of the methods declared by the services.
Create Stubs
Create Local objects that implements same methods as services.
Client Side
* gRPC: (Google Remote Procedure call)

## Slide 11
Run Server
Run a gRPC server to handle client call and start receiving requests.
Execute & Respond
Execute service methods according to incoming requests and encode response.
Run Client
Run the gRPC client to make the calls.
Work Flow
Call methods
Call the methods and wrap the parameters in the appropriate message type.
gRPC Server
Python Service
gRPC Stub
Python Client
Response
Request

## Slide 12: User Experience
Now it’s time to take a quick tour.
GitHub Repo

## Slide 13: Product
Our product provides automation to the testing process through a user friendly GUI.
User Friendly
Provides a user friendly GUI for both direct and HIL mode.
Support
We offer support to users to help them efficiently use our products.
Tested
Drivers and features are tested and reliable.
Open source
Anyone can enhance and tailor it to their needs.

## Slide 14: Growth Strategy
How will we scale in the future
Phase 1
Implementing and testing main peripherals and basic communications in direct mode such as DIO, PWM, ICU, UART and SPI.
Implementing and testing main peripherals and basic communications in HIL mode.
Phase 2
Implementing and testing Automotive communications, ADC and DAC in direct mode.
Implementing and testing Automotive communications, ADC and DAC in HIL mode.
Phase 3
Changing the communication medium to be wireless to enable over the air testing.
The user can connect to multiple test benches.

## Slide 15: Summary
Our system facilitates and automates the testing process which consequently results in:
June
28
Sunday
Early testing.
Ability to test complex scenarios.
Our system provides a GUI through which the user can choose to start testing via Direct Mode or HIL Mode.
The Direct Mode sends data frames cyclically, containing the data input by user to be updated on the target.
The HIL mode provides a test bench skeleton for the user where they can write scripts containing their own test cases.

## Slide 16: Team
Ahmed Refaat
Ahmed Zoher
Hazem Mekkawy
May Alaa
Waleed Adel
Supervisor
Ahmed Torky

## Slide 17: DEMO
Now it’s time for the demo.
GitHub Repo

## Slide 18: Thank You
BUG-z, Inc.

## Slide 19: QUESTIONS?
BUG-z, Inc.
Ahmed Zoher
Hazem Mekawy
Waleed Adel
May Alaa
Ahmed Refaat
ahmed.refaat.rashad@gmail.com
ahmed.o.zoher@gmail.com
mayelfkiy@gmail.com
waleedadelhassan@gmail.com
hazemfawzy.mekawy@gmail.com